Armazones 2k climatology
Tomek Bulik

---
What do we know
- Armazones: Atmoscope
- Armazones 2k:
  - Atmoscope like stations since May2015
  - November 2015:
    - 30 meter weather tower
    - ASC
    - Sun Moon photometer
    - Seismometer

---
10 meter station results
- Temperature
- Humidity
- Wind

---
Temperature distribution

---
Temperature extremes

---
Humidity distribution

---
Humidity extreme

---
Wind distribution

---
Wind extremes

---
Distribution of strong wind time

---
Data from 30 meter tower
- Wind profile
- Wind turbulence

---
Wind profile
V(h)=V(10{\rm m})\times {\ln(h/z_0) \over \ln(10{\rm m}/z0)
z_0=0.3\, {\rm m}
z_0=10^{-5}\, {\rm m}

---
Wind profile for strong winds
V(h)=V(10{\rm m})\times {\ln(h/z_0) \over \ln(10{\rm m}/z0)
z_0=0.3\, {\rm m}
z_0=10^{-20}\, {\rm m}

---
Wind power spectrum
Specification (Karman model)
Wrong!
My model – roughly fitting data.
s(f) = (IU)^2 { 4 L/U \over (1+70.8(fL/U)^2)^{5/6}}
I=0.25\ \ \ L=50m
I=0.01\ \ \ L=1000m

---
Wind conclusions
- Wind profile nearly flat: the air moves at nearly the same speed at all heights
- Wind power spectrum much flatter than assumed for construction
- Probably the observation state requirement can be relaxed, and the observation time will be increased

---
Summary
- Temprature is within operating range
- Humidity is typically low but not a big problem
- Strong wind episodes but the observing condition can likely be relaxed
- Still analyzing seismic data

---
Next steps
- Revive the ASC complex power
- Move the 30 meter tower to the actual LST location