## Slide 1
Markus Gaug, UAB
Site Climatology at ORM
What we already know...

## Slide 2: Site Climatology at ORM
Molecular profiles
Aerosol profiles
Weather data

## Slide 3: Molecular profiles

## Slide 4: Molecular profile
  Erec scales directly with optical transmission, i.e. integrated density from emission point to ground
  Erec scales approximately with ρc ≈ (hmed – hobs ) -2
  because of the modulation of the Cherenkov angle and
  median shower height.
    Bernlöhr, Astrop. Phys. 12 (2000), 255
  Aeff more complicated, needs simulations
Has effects on size of Cherenkov light pool (via shower altitude and Cherenkov angle) and transmission of Cherenkov light

## Slide 5: Molecular profile
Have excellent Data Assimilation models for La Palma (for free) for temperature and pressure (i.e. density):
Global Data Assimilation System (GDAS) from ground to 25 km a.s.l. ftp://arlftp.arlhq.noaa.gov/pub/archives/gdas1/
The NRLMSIS-00 model for 20 to 100 km a.s.l. http://ccmc.gsfc.nasa.gov/modelweb/atmos/nrlmsise00.html
The ECMWF has been tested by INFN Torino with very encourageing results http://weather.unisys.com/ecmwf/index.php
The IG2 model has been tested as well, but does not agree well at these altitude ranges (at least for temperature).
Has effects on size of Cherenkov light pool (via shower altitude and Cherenkov angle) and transmission of Cherenkov light

## Slide 6: Molecular profile
For molecular absorption not so clear...
Only O3, CO2 and NOX are (perhaps) relevant for us!
The IG2 model has been used by INFN Torino, claimed to be accurate, but not yet cross-calibrated with our instruments (or other databases).
The effect is small though (at least much, much smaller than the density effects)
Has effects on size of Cherenkov light pool (via shower altitude and Cherenkov angle) and transmission of Cherenkov light

## Slide 7: Molecular profile
For molecular absorption not so clear...
Only O3, CO2 and NOX are (perhaps) relevant for us!
The IG2 model has been used by INFN Torino, claimed to be accurate, but not yet cross-calibrated with our instruments (or other databases).
The effect is small though (at least much, much smaller than the density effects)
Has effects on size of Cherenkov light pool (via shower altitude and Cherenkov angle) and transmission of Cherenkov light
Credits: Piero Vallania, Bianca Binelli,
C. Bigongiari, F. Di Pierro, E. Papandrea

## Slide 8: Molecular profile
Ozone has been studied in detail at Izaña (Tenerife), 2400 m a.s.l.
E. Cuevas et al., “Assessment of atmospheric
processes driving ozone variations in the
subtropical North Atlantic free troposphere”,
Atmos. Chem. Phys., 13, 1973–1998, 2013

## Slide 9: Molecular profile
Ozone at high troposphere is correlated with a parameter called “Potential vorticitiy” (PV), measured in units of PVU.
Situations with PVU>1.0 indicate stratospheric intrusions into the upper troposphere and hence high O3 concentrations.
E. Cuevas et al., “Assessment of atmospheric processes driving ozone variations in the subtropical North Atlantic free troposphere”, Atmos. Chem. Phys., 13, 1973–1998, 2013

## Slide 10: Molecular profile
Ozone at high troposphere is correlated with a parameter called “Potential vorticitiy” (PV), measured in units of PVU.
Situations with PVU>1.0 indicate stratospheric intrusions into the upper troposphere and hence high O3 concentrations.
E. Cuevas et al., “Assessment of atmospheric processes driving ozone variations in the subtropical North Atlantic free troposphere”, Atmos. Chem. Phys., 13, 1973–1998, 2013
PVmax maps for winter (JFM), spring (AMJ), summer (JAS) and autumn (OND) in the period 1988–2009.

## Slide 11: Molecular profile
E. Cuevas et al., “Assessment of atmospheric processes driving ozone variations in the subtropical North Atlantic free troposphere”, Atmos. Chem. Phys., 13, 1973–1998, 2013
Stratospheric
intrusions

## Slide 12: Molecular profile
Cross-correlation with MAGIC weather station
GDAS combined with NRLMSIS-E
Perfect match for pressure comparison
Systematic shift for temperatures can be explained by local ground effects (inverse for day-time data)
Even correlation for humidity is good
(difficult because of very local variation)

## Slide 13: Molecular profile
Cross-correlation with the MAGIC LIDAR
GDAS combined with NRLMSIS-E
The LIDAR is sensitive to the molecular profile during clear nights
We see a significant improvement from linear fits to “GDAS-fits”.
The GDAS fits yield correct χ2 distributions!

## Slide 14: Molecular profile
Cross-correlation with the MAGIC LIDAR
GDAS combined with NRLMSIS-E
The LIDAR is sensitive to the molecular profile during clear nights
We see a significant improvement from linear fits to “GDAS-fits”.
The GDAS fits yield correct χ2 distributions!

## Slide 15: Molecular profile Simulation input for the MC studies
Simulation input for the MC studies
GDAS combined with NRLMSIS-E
The LIDAR is sensitive to the molecular profile during clear nights
We see a significant improvement from linear fits to “GDAS-fits”.
The GDAS fits yield correct χ2 distributions!

## Slide 16: Molecular profile
Simulations and first result are shown on Wednesday morning by Federico di Pierro (INFN Torino)

## Slide 17: Aerosol profiles

## Slide 18: Aerosol profiles
Aerosol enhancements of ground layer (“calima”) and clouds (cumulus and cirrus)
Strong dependency on time and altitude
Strong energy dependency in case of clouds
Have analyzed more than 3 years of good quality MAGIC LIDAR data
Taken synchroneously with science data (5 deg. offset)
Has potentially strong effect on extinction of Cherenkov light

## Slide 19: Aerosol profiles
3 years of continuous MAGIC LIDAR measurements
Almost 10 years of the TNG dust counter
20 years of Sun photometer measurements (Izaña, Tenerife)
Extremely detailed aerosol characterization with state-of-the-art equipment at IARC (Izaña, Tenerife)
Are very well studied on La Palma, using:

## Slide 20: Aerosol profiles
The Island of La Palma is
affected by:
the trade winds
below 1800 m a.s.l.
the descending dry air
transported by the
Hadley cell along the
tropopause above
1800 m a.s.l.
La Palma

## Slide 21: Aerosol profiles
PM10 distributions obtained at Izaña, Tenerife (2400 m a.s.l.)
Threshold
for extremely
clean environments
E.Cuevas and J. M.Baldasano,
“Report on the Incidence of African dust intrusions at the Astronomical Observatories of the Canary Islands:
characterization and temporal analysis”, Izan ̃a Atmospheric Research Centre of AEMET and the Earth Sciences Department, 2009.

## Slide 22: Aerosol profiles
Aerosol enhancements of ground layer (“calima”) and clouds (cumulus and cirrus)
Strong dependency on time and altitude
Strong energy dependency in case of clouds
Have analyzed more than 3 years of good quality MAGIC LIDAR data
Aerosol Transmission over time from MAGIC LIDAR (absolutely calibrated with the Sun photometer data from Izaña)
Summer Calima periods

## Slide 23: Aerosol profiles
Aerosol enhancements of ground layer (“calima”) and clouds (cumulus and cirrus)
Strong dependency on time and altitude
Strong energy dependency in case of clouds
Have analyzed more than 3 years of good quality MAGIC LIDAR data
Aerosol Transmission probability map from MAGIC LIDAR
Clouds
Calima

## Slide 24: Particle size distributions
10 nm
100 nm
1 μm
Scattering
enhanced:
~ 40 cm-3
Measurements at Izaña
(Tenerife) support idea of
“aged aerosols”
that travel downwards
Rodríguez S. et al., “Atmospheric nanoparticle
observations in the low free troposphere during
upward orographic flows at Izaña Mountain
Observatory”,
Atmospheric Chemistry and Physics 9 (2009) 6319-6335

## Slide 25: Particle size distributions
10 nm
100 nm
1 μm
Scattering
enhanced:
~ 40 cm-3
Simplified (pure “Mie”) extinction coefficient
k(λ,r) =Qext(n,r,λ) πr2 N
mode: 50 nm

## Slide 26: Particle size distributions
CAMT extinction measurements: agree well with Izaña data
Lombardi G. et al.,
“El Roque de los Muchachos Site Characteristics II:
Analysis of atmospheric dust and aerosol extinction”,
A&A (2008) arXiv:0802.3947v2

## Slide 27: Aerosol Extinction coefficients
20 years data base from the Carlsberg Meridian Telescope
García-Gil A., Muñoz-Tuñón C., Varela A. M. “Atmosphere Extinction at the ORM on La Palma:
A 20 yr Statistical Database Gathered at the Carlsberg Meridian Telescope”, PASP 122 (2010) 1109.

## Slide 28: Aerosol optical extinction coefficients
20 years data base from the Carlsberg Meridian Telescope
García-Gil A., Muñoz-Tuñón C., Varela A. M. “Atmosphere Extinction at the ORM on La Palma:
A 20 yr Statistical Database Gathered at the Carlsberg Meridian Telescope”, PASP 122 (2010) 1109.

## Slide 29: Aerosol AODs
Converting the
particle size distributions
to extinction coefficients
and converting these
into AODs
yields a consistent
picture between the
different data sets available for
the clear night at La Palma

## Slide 30: Aerosol profiles
Has been studied for MAGIC only by Garrido et al. (ICRC 2013, ID 0465 and arXiv:1308.0473) and is part of the CTA Atmospheric Calibration Strategy: COM-CCF/130311 https://portal.cta-observatory.org/recordscentre/Records/COM/COM-CCF/lidar_loi2.pdf
Needs confirmation and extension of energy range for CTA
Impact of aerosol intrusions and clouds on IACT data

## Slide 31: Impact of aerosol intrusions on IACT data
Different simulated cases of “calima”:
OD*15
OD*30
OD*0.1

## Slide 32: Impact of aerosol intrusions on IACT data
Clear night seen with MAGIC LIDAR

## Slide 33: Impact of aerosol intrusions on IACT data
Calima seen with MAGIC LIDAR

## Slide 34: Impact of clouds on IACT data
Simulated “cloud” at 3 different altitudes:
6 km (cumulus)
10 km (cirrus)
14 km (volcanic debris)

## Slide 35: Impact of aerosol intrusions on IACT data
Cloud (and calima!) seen with MAGIC LIDAR

## Slide 36: Impact of aerosols (calima and clouds) on IACT energy threshold
Cirrus (10 km)
Volcanic debris
(14 km)

## Slide 37: Impact of aerosols (calima and clouds) on IACT on energy scale
Cirrus (10 km)
Volcanic debris
(14 km)

## Slide 38: Impact of aerosols (calima and clouds) on IACT reconstructed spectral index

## Slide 39: Impact of aerosols (calima and clouds) on IACT reconstructed flux

## Slide 40: 12 years of MAGIC weather station data

## Slide 41: Wind measurements
Large data base of weather data from the roof of the MAGIC control house.
Still need to study the wind at different altitudes (and possibly different points across the CTA area).

## Slide 42: Wind measurements
Wind comes preferably from ESE
Storms come preferably from a wide range covering E-S-W
only v<50 km/h,
linear scale
all data
v<140 km/h,
log scale

## Slide 43: Wind measurements
30 m tower at the LST site would be needed to measure the altitude profile.
Included the tower in the first call to the Spanish FEDER funds (to be released in Autumn this year).
Some conflict with the LST1, but are confident to collect still enough data before the mirrors are mounted.

## Slide 44: Humidity measurements and rain
Noted some hysteresis in our humidity sensor
Also rain is possible with RH<90% !!
Need additional rain sensors

## Slide 45: Rain and humidity sensors
Up to now, rain/humidity is only measured at one point (roof of MAGIC control house)
However, clouds drift sometimes up the mountain, may affect parts of the CTA array without being seen at the MAGIC site. Not much known about statistics of this effect.
Plan to install several rain/humidity sensors across the CTA area and characterize gradients across the terrain.