## Slide 1: Status of IFAE/UAB Raman LIDAR
Lluís Font and Markus Gaug
UAB & CERES-IEEC
Central Calibration Facilities meeting
Barcelona 20-23 June 2016

## Slide 2: Overview
The concept
Recycle a former CLUE telescope and container to build and advanced Raman LIDAR optimized for CTA
2 + 2 configuration:
  355 nm + 532 nm elastic channels
  387 nm + 607 nm N2 Raman lines
Atmospheric molecular and aerosol transparency as a function of range and wavelength.
Laser: Brilliant Compact Q-Switched Nd:YAG 1064nm + frequency tripler head Rate:10 Hz Pulse:5 ns Beam divergence:0.5 mrad
Parabolic mirror f = 180 cm => f/D = 1
Dichroic guiding mirrors  coaxial
Polychromator home made
Acquisition: standard LICEL units

## Slide 3: Overview
The strategy
IFAE/UAB prototype
LUPM prototype
Long-term testing @ La Palma
(1 year of robotic operation)
Final Raman LIDAR design
(based on former CLUE experiment)

## Slide 4: Overview
The funding situation
  Funding for LIDAR prototype still is insufficient this year (as all Spanish funding proposals in 2016).
  Funds for final LIDAR will come from FEDER funds
  in 2017-2018.
The team
+ Markus Gaug (UAB)
+ Oscar Martínez (IFAE) (Eng)
+ Oscar Blanch (IFAE)
+ Oriol Calpe (UAB) (Undergraduate)
+ Michele Doro (INFN Padova)
+ Lluís Font (UAB)
+ Merve Colak (IFAE) (PhD student)
+ Scott Griffiths (IFAE) (Postdoc)
+ Manel Martínez (IFAE)

## Slide 5: Status prototype
Hardware
Mirror characterized
Liquid light guide characterized
Guiding mirrors (dichroic) + alignment in zenit. Monochromator used
Driving system not robotic yet
Polychromator finished. Characterization studies on-going
Laser being repaired. Near range solution and fine-alignment postponed. Back on track soon (within 2 weeks)


## Slide 6: Status prototype
Software
Library to read Licel files ready
Internal communication translated from Labview to C (in process)
Documentation
Finished one bachelor thesis on pre-alignment (Eudald Font)
Another bachelor thesis on polychromator characte-rization is on-going (Oriol Calpe)
Constantly update a LIDAR TDR
ICDs created (except for the one with ACTL)

## Slide 7: LIDAR alignment

## Slide 8: LIDAR alignment
23/07: “calima”

## Slide 9: Documentation

## Slide 10: Polychromator

## Slide 11: Polychromator

## Slide 12: Polychromator
Characterization test set up
Xe source
Colimator
Filter wheel
Monochromator
Shutter
Liquid light guide
Polychromator
PIN diode

## Slide 13: Polychromator
607nm
Preliminary results
607 nm

## Slide 14: Polychromator
607nm
Preliminary results
355nm 387nm 532nm 607nm

## Slide 15: Outline
Polychromator characterization will finish soon (2 weeks).
Near range solution and fine alignment will start before summer holidays.
Making it robotic.
Prototype should be ready for long term testing by mid 2017