## Slide 1
The ASTRI prototype:
a pathfinder Dual-Mirror telescope for the CTA-SST array
Rodolfo Canestrari for the ASTRI collaboration
INAF-Astronomical Observatory of Brera
An overview on the optical design, telescope structure & mechanics and mirrors

## Slide 2
This work has been performed by INAF in collaboration with:

## Slide 3
The optical design
F#: 0.5
f: 2.15 m
Pixel: 0.16°
FoV: 9.6°
Plate-scale: 37.5 mm/°
PSF: EE80% < 6 mm
Effective area: 6.5 m2
3 m
1.8 m
4.3 m
M1 radius: 8.2 m
M2 radius: 2.2 m
DET radius: 1 m

## Slide 4
The telescope
Item | Mass [kg]
M1 dish | 4.000
Mirrors and supports | 555
M2 dish | 550
M2 mirror | 200
Camera | 50
Mast | 560
Ballast structure | 800
Counterweight | 4.400
Fork and tower | 4.000
Total | 15.115
Preliminary mass budget

## Slide 5
The quadrupod
The quadrupode legs with the radial bracing counteract the lateral deformations while the central tube increase the torsional stiffness.
Structural analyses

## Slide 6
1st natural frequency: 8.5 Hz
The dish – RIBBED PLATE
400 mm thick steel plate composed of two halves. Easy manufacturing and assembly.
Structural analyses

## Slide 7
Sensitive analyses to understand the thermo-elastic behavior:
±1°C linear gradient along dish thickness
±1°C linear gradient along tower
±1°C linear gradients along central tube
±1°C linear gradients along mast
Important contribution to mirrors misalignment
Significant contribution to telescope pointing
Negligible overall effects
Negligible overall effects
1
2
3
4
Structural analyses

## Slide 8
Mechanicals systems - driving
The azimuth assembly is composed by two ball bearings axially preloaded.
The driving system is done with two pinions coupled with a rim gear.
The elevation assembly is composed by two shafts with preloaded tapered roller bearings.
The driving system is done with a linear actuator with a gear box and preloaded ball screw.

## Slide 9
Mechanicals systems - measuring and safety
Absolute encoders (HEIDENHAIN RON 786) interfaced with GALIL controller (with adjustable PID parameters)
Safety system concept
Electromechanical stow pins
0°
-270°
-275°
+270°
+275°
altitude
azimuth

## Slide 10
Primary mirror (M1)
18 hexagonal shaped mirrors (11.2 m2)
850 mm face-to-face, 1 m diagonal
3 types of segments
2 actuators + 1 fixed point
Secondary mirror (M2)
1 monolithic mirror, 1.8 m diameter (2.5 m2)
3 actuators + 3 lateral constrains
Reimaging system (CAM)
500 a-symmetric pyramids, 14x14x2.5 mm3
Coatings
CAM
The optical surfaces

## Slide 11
The optical surfaces - support and alignment
2 actuators designed to minimize the cost:
  Eccentric shaft
  Encoder
  Stepper motor
  Gear box
Mounting/dis-mounting safe procedure
Primary mirror segments

## Slide 12
Secondary mirror (monolithic)
3 actuators connected to the mirror with load spreader (whiffletree)
3 lateral constrains support the lateral component of the mirror’s weight (varying with the elevation)
The optical surfaces - support and alignment

## Slide 13
Example of M1 segments alignment procedure
Take a picture of the star
Move one M1 segment of a known amount
Take a picture of the star
Subtract the two images in a “smart Conconi way”
(See the picture on the side)
Find the barycenter
Repeat for each segment
The optical surfaces - support and alignment

## Slide 14
Manufacturing process: “Cold slumping 2.0”: hot pre-shaping + cold
Structural implementation: sandwich panel with thin glass skins
The optical surfaces - mirrors

## Slide 15
The mirror design is being evaluated by very detailed FEA
Mirror’s edge
Mirror’s interfaces
The optical surfaces - mirrors

## Slide 16
Panels Results | 
Radius of Curvature | 32 ± 0.1 m
Surface accuracy | 80% energy in < 0.5 mrad
Reflectivity | > 80% range 300 to 600nm
Coating | Al + SiO2
20 mirrors panels have been successfully produced in less then 1 month (Dec 2011)
The optical surfaces - mirrors
All mirrors have been measured with 2f method  D90 < 1 mrad
Now, under repetition after the coating
Cold slumping technology
Weight: 11.75 kg

## Slide 17
Some preliminary results coming from previous developments with FLABEG:
Microroughness has been measured:
[5.2mm÷100mm]  s = 1.6 nm rms
[600÷10] mm  s = 0.4 nm rms
Very good performances on spherical profiles, 300 mm scan length.
PV error wrt best sphere = 6 mm
Capability of very short radii (down to 1.5 m)
The optical surfaces - mirrors
Hot slumping technology

## Slide 18
RoC 5 m
20 mm
14 mm
The optical surfaces - mirrors
530 x 530 mm mirror segment, 5 m RoC assembled with standard Al honeycomb is possible.
Standard honeycomb cut in proper way to accommodate the curvature, but astigmatic deformations may occur.
Special honeycomb under evaluation to minimize deformations.
Cold slumping 2.0 technology

## Slide 19
The optical surfaces - mirrors
Bended glass from FLABEG has been realized. The delivery is foreseen in these days.
Design of the master for the mirror integration ready.
Offer for “special honeycomb” obtained. It is done upon purchase order  11 weeks for the delivery!!

## Slide 20
2 sets of engineering models delivered on December 2011.
12 pyramids with only 2 surfaces polished
15+ pyramids with all 6 surfaces polished
Material: glass BK7
1st set of engineering models for measurement tests delivered on January 2012.
All 6 surfaces polished!
Material: glass LAKN9
The optical surfaces - light guides

## Slide 21
Enhanced reflectivity for M1
2 layers: Al + SiO2
3 layers: Al + SiO2 + ZrO2
5 layers: Al + 2(SiO2 + TiO2)
31 layers: 15(TiO2 + SiO2) + TiO2
The optical surfaces - coatings
Simulated reflection

## Slide 22
Anti-reflection for light guides:
  4 layers: 2(ZrO2 + SiO2)
The optical surfaces - coatings
Handling tool for deposition
Simulated transmittance