## Slide 1: CTA Candidate site(S) in NAMIBIA
Namibia/SA CTA task team
SSC, Heidelberg, 3-5 April, 2013
Presenter: R Steenkamp
Special thanks to: P Krüger, T&S Hanke & I Davids

## Slide 2: Introduction
Southern Africa offers
  some of the world’s best sites for astronomy
  good infrastructure and low risks for scientific investment
  a proven track record in hosting and attracting world-class astronomical telescopes (H.E.S.S., SALT, KAT-7, MeerKAT, SKA)
Many excellent sites exist in Namibia – reduced to two sites:
  The Aar/Kubub site(s) – from now on only referred to as the `Aar site’
  Site(s) close to the H.E.S.S. site – from now on only referred to as the `Göllschau site’
Currently, the Aar site is the focus of investigations since
  it is considered to be the superior site by us, and
  the characteristics of the Göllschau site are well known

## Slide 3: Site Location I (Maps)
Aar
Göllschau
Capital
with
Airport
(40km)
Harbour
(120km)
&
Airport
(112km)
Railway
Station

## Slide 4: Site Location I (Orography)
Orography of the Aar/Kubub Plateau
Aar (East)
(16.4820ºE, -26.682ºS)
(1637±10) m asl
Aar (West)
(16.4530ºE, -26.691ºS)
(1633±13) m asl
Kubub
(16.4235ºE, -26.704ºS)
(1663±12) m asl

## Slide 5: Site Location I (Images: Aar)
Aar site: Farm Aar
Aar site: Farm Kubub

## Slide 6: Site Location I (Images: Aar)
Aar site: Valley between the Aar and Kubub plateaus
(suggested location of access road onto the site)

## Slide 7: Site Location I (Images: Göllschau)
Göllschau site: Farm Göllschau
View of Mt Gamsberg from HESS site

## Slide 8: Site Location II
Aar (West)
(16.4530ºE, -26.691ºS)
(1633±13) m asl
Kubub
(16.4235ºE, -26.704ºS)
(1663±12) m asl
Aar (East)
(16.4820ºE, -26.682ºS)
(1637±10) m asl
Implantation of CTA array on Aar/Kubub

## Slide 9: Site Location II
Göllschau: HESS
(16.4993ºE, -23.2715ºS)
(1815±7) m asl
Göllschau: Isabis
(16.490ºE, -23.340ºS)
(1767±10) m asl
Implantation of CTA array on Göllschau

## Slide 10: Site Location II
Conformity with (Geographical & Topographical) Requirements:
Layout | Latitude [-40º,-20º] | Height a.s.l (mean±stdev) [1500,3800] m | Area [>10 km2] LinExt [>3 km] | Gradients | Δh between Highest & lowest tel. | Conform
Aar east | -26.682º | (1637±10) m | White dotted circles in previous diagrams represent area > 10 km2 and diameters of 3.6 km | Local gradients in area of sites <3.5% Local gradients around telescope & buildings <2% | 48 m | Yes
Aar west | -26.691º | (1633±13) m |  |  | 71 m | Yes
Kubub | -26.704º | (1663±12) m |  |  | 69 m | Yes
Göllschau:HESS | -23.2715º | (1815±7) m |  |  | 34 m | Yes
Göllschau:Isabis | -23.340º | (1767±10) m |  |  | 51 m | Yes

## Slide 11: Site Location III
Geotechnical conditions (Aar)
Most of the Aar plateau consists of quartzitic sandstone interlayered with shales (depth ~ 20 m)
Telescope foundations on stable bedrock
Drainage removes water from the proposed site
Special consideration (Kubub)
Sand-filled depression on Kubub  Aar-west/-east implantation more desirable
Aar
(West)

## Slide 12: Weather Conditions I : Cloud cover
Percentage of completely clear nights ( 0% cloud cover):
Aar: (80±5)%
Göllschau: (70±5)%
Percentage of partially clear nights (<20% cloud cover):
Aar: (85±5)%
Göllschau: (75±5)%
 | Göllschau |  | Aar | 
Moonless hours | 1602 |  | 1584 | 
Cloud Cover | <20% | 0% | <20% | 0%
Moonless & cloudless hours | 1202±80 (75±5)% | 1121±80 (70±5)% | 1346±48 (85±5)% | 1267±48 (80±5)%
Hours available for observation* | 1173±80 | 1097±80 | 1275±54 | 1208±53
* Hours with too high humidity, too strong wind and too high temperature subtracted.

## Slide 13: Weather Condition II: Wind
Percentage of night hours wind < 36 km/hr (10 min average):
Aar: >97-99%
Göllschau: >99%
Probability of > 200 km/hr gusts (1 sec gusts):
Aar: never
Göllschau: never
WIND | Observation Time Lost | 
 | Göllschau | Aar
% of night hours win < 36 km/h (10 min average) | < 0.5% | Atmoscope: < 0.2% SENES: 3%
Probability of > 200 km/h (1 sec gust) | never | never

## Slide 14: Weather Conditions III: T, RH, precipitation
Percentage of time temperature and humidity within operation range:
Temperature in range >99% of the time at both sites
Humidity condition satisfied when dew point is not too large for observation.
  Time loss of clear nights
    Aar: (2.2±0.8)% Göllschau: (2.2±1.3)%
Percentage of nights with snow on ground:
  Aar: light and sparse (~3h/yr)
  Göllschau: never
Conformity with extreme temperature, humidity and precipitation survival requirements:
  Temperatures -20 to 40ºC: SENES: -5 to 35ºC for both sites
  Humidity 2 to100%: always for both sites
  Precipitation in 24h < 200mm: always for both sites

## Slide 15: Night Sky Background
Namibia sparsely populated with very little artificial light pollution
Göllschau:
  Windhoek to the north-east may have effect at large zenith-angles
Aar:
  Site is located in one of the darkest regions of the subcontinent
  Shielded from road(s) and village of Aus.
LONS for both sites:
  23.5±0.2 mag/arcsec2 in B
  22.5±0.2 mag/arcsec2 in V
NB: sites are exposed to the natural brightness of the Milky Way

## Slide 16: Natural Hazard Risks
Earthquakes:
Both sites located in one of the most
seismic stable regions on Earth
Wind storms:
Never occurs at both sites
Hail storms:
Lowest risks for both sites (SENES: none)
Sand storms:
Aar less risk than Göllschau
Recent study by UNAM’s Geology Department:
  “There is no evidence for any occurrence of sandstorms…”
  “…no ventifacts, sand ramps or sand traps.”
  “Man-made structures do not show any signs of abrasion by sandstorms…”

## Slide 17: Social/Political Risks I
Political stability of Namibia:
Politically stable – no history of conflict since independence.
All regime changes since 1990 incident free as result of national elections.
“B” Euler-Hermes risk grade – “Low Risk”

## Slide 18: Social/Political Risks II
Crime in Namibia:
The crime rates in the rural areas \quite low – proposes sites very safe
The crime rate in Namibia much lower than most countries around the globe
Numbeo: Namibia has Crime & Safety Indices similar to the Netherlands.
However, precautions against burglary should be undertaken at the sites.
http://www.numbeo.com/crime/rankings_by_country.jsp

## Slide 19: Social/Political Risks III
Import regulations:
Import & Export Control Act, Act 30 of 1994 –import permits pre-obtained
All imports subject to importation duties -- unless a rebate/exemption pre-negotiated
Any other important consideration:
  Namibian officials at Ministry:
    similar concessions extended to H.E.S.S. & SKA possible for CTA…

## Slide 20: Infrastructure I
Electricity:
Southern African Power Pool
  connecting stations in Keetmanshoop and Windhoek.
Detailed quotations requested from NamPower (and paid for) in 2012
  still pending
Last week: Ministry officials in contact with NamPower MD
…however, certain estimates can be made:

## Slide 21: Infrastructure I
Electricity (Aar):
Two 132kV lines passing the farm Aar.
The closes substation just north of Aus, connecting it with a 33 kV line
A new power line, from Aus to farm Aar would have to be built.
Rough estimate: Such a 20 km line will cost about N$3.6 million (~€360,000)

## Slide 22: Infrastructure I
Electricity (Göllschau):
H.E.S.S. is already connected to NamPower via a 33 kV power line
A short power line need to be constructed towards the eventual site

## Slide 23: Infrastructure II
Water:
Aar:
  Boreholes on Farm Kubub (35 m3/hour)  sufficient water available
    needs to be pumped up to the plateau & stored in reservoir
Göllschau:
  General use: boreholes can deliver slightly more than 5 m3/day
  Construction: Farm Weissenfels has a dam.

## Slide 24: Infrastructure III
Data network:
Namibia has well-developed optical fibre network
International bandwidth supplied by sub-marine cables:

## Slide 25: Infrastructure III
Data network (continued):
Telecom Namibia will construct relevant network extension(s):
  30 km fibre AusAar and/or 90 km fibre from RehobothGöllschau)
      N$805,000 (~€67,000) once-off set-up fee
Telecom Namibia quotations for highly redundant, fully protected 1 Gbps link:
  N$5,071,549/month rental (~€423,000/month)
Quotations also for 5 & 10 Gbps links
Cheaper, alternative designs with less guarantees available

## Slide 26: Accessibility
Distance to airport:
Aar: Lüderitz airport (~140 km) – mostly tarred road
Göllschau: Hosea Kutako International airport (~140 km) – mostly gravel
Nearest town to live:
Aar: Aus (~30 km)
Göllschau: Windhoek (~100km dirt road) or Rehoboth (90 km dirt road)
Nearest hospital:
Aar: Clinic in Aus – larger hospitals in Lüderitz & Keetmanshoop
Göllschau: Hospitals in Windhoek & Rehoboth

## Slide 27: Site Ownership
Procedure to obtain permission for use:
Lease contract to be negotiated with relevant landowner/farmer
Aar:
  CTA can be build entirely on Farm Aar but access road must be through Farm Kubub (owners gave verbal permision)
Göllschau:
  CTA can be built on Farm Göllschau or partially also on Farm Weissenfels
Construction permits needed:
No construction permits are needed as all sites do not fall under any municipal areas
Nevertheless, it is advised to adhere to local building codes

## Slide 28: Political support of Host Country I
Clear support fexpressed several times by government(s) at regional, national and local levels:
Regionally, the issue of CTA South has been repeatedly discussed between government officials tasked with Science & Technology from Namibia & South Africa.
Nationally, statements of support ranging from the original letter of support by the PS of the Ministry of Education to support stipulated in the inauguration speech of H.E.S.S. II by the Minister of Education.
Officials of the Ministry of Education signed the CTA Declaration of Intent (DoI) in 2012
Public monetary resources was made available for site investigations, and very recently towards the appointment of a Namibian CTA project manager.
Locally, support was expressed by a Namibian regional councillor at a recent meeting of the Namiba/SA CTA team in Aus.

## Slide 29: Political support of Host Country II
Last week: I was reminded by officials to mention:
  The Namibian government can issue visas at no charge.
  The Namibian government is open to discussions vis à vis importation duty & tax concessions
    The latter may result in CTA saving millions with the aid of tax concessions

## Slide 30: Conclusion
Strong political support exists within Namibian & Region (esp. South Africa)
Well developed transport, power and telecommunications networks
Manpower, especially unskilled and semi-skilled labour is quite cheap
Göllschau site close to capital & already has much of infrastructure in place  lower risk site
Aar site more remote, but has better transport infrastructure, and is a better from astronomical PoV
Both sites: excellent & low risk options to host CTA South
All the proposal documents, reports, presentations, photos etc. are available at https://portal.cta-observatory.org/WG/SITE/SitePages/NamibiaInfo.aspx

## Slide 31: Epilogue