## Slide 1
David Bristow, Stephen Brown, Paolo Calisse, Stefano Stanghellini, Wolfgang Wild, Nick Whyborn, Roberta Zanin March 14, 2023
MSTN-15 position: CTAO point of view
Notes: Comet NEOWISE. NEOWISE stands for Near Earth Object Wide-field Infrared Survey Explorer. That's the Earth-orbiting satellite used to discover the comet designated C/2020 F3, but you knew that.

## Slide 2: Northern array: as-requested coordinates
MSTN-15 position needs to be modified because in conflict with our internal LSTN-04 access road
IAC suggests a position 10 m away in the NW direction toward LSTN-04

## Slide 3: Northern Array: scientific assessment
  When considering the IAC-suggested position
  the MSTN-15 would suffer up to 10% shadowing (loss in optical effective area)
    when the LST is pointing both towards the MSTN-15 and along its line of sight or at zenith
    at an MST zenith distance which is 5-8 degree smaller than the one found for the original MSTN-15 position
     shadowing becomes relevant at 52 deg
  Science-wise. Very limited science cases: the LST and MST sub-arrays operatining independently at specific direction
  Operations-wise. Two options: 1. the production of the MST-sub-array IRFs will have to take the LST pointing into account, and model the shadowing
  2. implement appropriate scheduling constraints

## Slide 4: Compromise solution
With the aim of keeping the best possible symmetry and limited as much as possible the shadowing, CTAO proposed a compromise solution on December 24, 2022
  This solution keeps into account the human-made constraints, safety regulations
  This solution is acceptable for the MST consortium despite the fact that the radius between the swing radius and the fence has been reduced to the safety minimum in some area
    Despite the locally limited reduction of the margin between the fence and the swing radius, the overall 3m margin generally allows to keep a similar level of flexibility for access and maintenance, as demanded by MST.

## Slide 5: MSTN-15 CTAO-proposed solution

## Slide 6: Engineering Concept Study MSTN-15
Coordinates at Telescope Foundation Centre – X = 217611.8 – Y = 3185066.7
Plan Drawn for Option 1

## Slide 7
Engineering study on the MSTN-15 position
Section Drawn for Option 1

## Slide 8: Concept Study - Option 1
Option 1 - Concept Study based on the preferred position –
  Centre of Telescope Foundation X = 217611.8 – 3185066.7
  Level at top of Foundation 2174.5m against 3metre high retaining wall to the LSTN4 Access road and to each side of the CMS Foundation at a variable height.
  Camera removal from CMS with Mobile Crane from LSTN4 Access road.
  Downside increased quantity of earth removal and extensive Retaining Wall Structure Construction.
  Access to Foundation from LSTN4 Access Road from the North West.
  Note: A detailed Engineering study is required to this Concept Study.

## Slide 9: Concept Study – Option 2
Option 2 - Concept Study based on the preferred position –
  Centre of Telescope Foundation X = 217611.8 – 3185066.7
  Level at top of Foundation 2171.5m to Road Level LSTN4 Access Road.
  Improved Access for Camera Removal from CMS from LSTN4 Road.
  Downside increased quantity of earth removal and extensive Retaining Wall Structure Construction.
  Consider this has a major cost implication on current budget.
  Note: A detailed Engineering study is required to this Concept Study.

## Slide 10: Concept Study – Option 3
Option 3 - Concept Study based on the preferred position –
  Centre of Telescope Foundation X = 217611.8 – 3185066.7
  Level at top of Foundation 2177.5m. To give access at ground Level from MAGIC Road.
  Downside – 6metre high retaining wall required against the LSTN4 Access road and to each side of the CMS Foundation at a variable height.
  Downside increased quantity of earth fill under the CMS and against retaining wall to LSTN4 road.
  Consider this may have a cost implication of current budget.
  Note: A detailed Engineering study is required to this Concept Study.

## Slide 11: Wrap up
The central position of the MST is engineering-wise very complex independently from the exact decided position

## Slide 12
R. Zanin
PC - July 5, 2021
Alpha Configuration
Thank you!

## Slide 13: MSTN-15

## Slide 14: Northern Array: central MST position
Credits to Tobias Kleiner, Orel & Gernot

## Slide 15: Northern Array: central MST position
Credits to Tobias Kleiner, Orel & Gernot