Image parametrisation:
2D Image Fitting
Image parametrisation:
2D Image Fitting
Clara Escañuela Nieves
27th October 2023
DataPipe meeting

---
Motivation
Truncated images: Energetic events with large impact distance (large leakage, large centroid distance from camera centre)
Hillas parametrisation:
- Limited by physical boundaries of the camera
- Including truncated images lead to large uncertainties in reconstruction
- Subject to biases from non-operational pixels
Goal
- Improve reconstruction at high energy
- Improve the robustness under NSB and hardware issues

---
Method
Image cleaning
Hillas parameters
Centroid
Length and width
Orientation
Intensity
Skewness

---
Method
Image cleaning
Hillas parameters
Image dilation
Seeds: Hillas
Model? Skewed gaussian
Fit boundaries
Image fitting

---
Likelihood
Neg log likelihood minimizer (iminuit)
Likelihood
Updated Hillas parameters
+ uncertainties
+ goodness of fit
+ Fit validity

---
Hillas parameters

---
Hillas parameters

---
Hillas parameters

---
Simulations for testing
Prod6 Paranal 14 MSTs in alpha configuration
Image filtering:
- Size > 50 pe
- Non-zero pixels > 7
- Telescope multiplicity > 4
- Centroid cut < 0.8 m
- Leakage cut < 0.1
Cut on truncation

---
Performance

---
Summary and discussion
Some more unit tests? Tests to show situations where the fit is better than Hillas
So far other FlashCam has been tested, we need to include other telescopes
Tests with increasing NSB, broken pixels, etc. Is it robust?
Method speed? Could it be faster? Probably yes...
Complete performance test once it is fully integrated in ctapipe