## Slide 1
CCF/CTA Calibration Meeting
T. Mineo– CCF/CTA Meeting, Barcelona, 26-28 October 2015
Muons for ASTRI
Teresa Mineo, Cettina Maccarone
– INAF/IASF-Palermo, Italy
for the ASTRI Collaboration & the CTA Consortium
Universidade de São Paulo
Instituto de Astronomia, Geofisica
e Ciencias Atmosferica

## Slide 2
Simulations
T. Mineo – CCF/CTA Meeting, Barcelona, 26-28 October 2015
CORSIKA | N. Event | 2000000 (m+, m-)
 | Site | Paranal
 | Viewcone | 4 deg
 | Pointing | Zenith
 | spectral index | 2.0
 | energy range | 6 GeV-1 TeV
 | Max Distance | 2.1 m
 | Starting altitude | 500 m above M1
 | Background | 20x106 ct/s/pixel
ASTRI-SIMULATOR: | includes the mirror reflectivity, the SiPM PDE, the PMMA window transmission, some mounting structure over the mirror | 
ANALYSIS SOFTWARE | Fortran + IDL code | 

## Slide 3
Steps of the analysis
T. Mineo – CCF/CTA Meeting, Barcelona, 26-28 October 2015
For all events, cut pixels below 0.5xMaximum or 5xRMS of the background; cut isolated pixels
3) Clean the raw image with a constant value equal to the 1xRMS of the background
2) If more than 4 pixels are left, the centre and the radius are obtained with Taubin method, minimizing the displayed function. This step cut ~20% of the events
(a,b)
R
4) Compute the radial profile (ArcWidth) and fit it with a Gaussian

## Slide 4
Steps of the analysis
T. Mineo – CCF/CTA Meeting, Barcelona, 26-28 October 2015
5) Compute the intensity profile along the ring; Fit it with the Vacanti function
6) Compute the reconstruction errors on the muon parameters after a selection on x and on the ring radius (x<0.05 & R>0.8o). This cut 94% of the events
low statistics
It makes the fitting faster
it provides values of the impact parameter sufficiently adequate for the first iteration
The second iteration will consider the correct
functions, investigating in a range close to the value given by the fit with Vacanti.

## Slide 5
Results: Reconstruction error on the zenith angle
T. Mineo – CCF/CTA Meeting, Barcelona, 26-28 October 2015
Zen_sim = Simulated zenith angle
a,b = coordinate of the ring center in pixel
Pix = 0.17o pixel size
Fitting with a Gaussian gives the maximum at 0.18o and the sigma 0.18o

## Slide 6
Results: Reconstruction error on the energy
T. Mineo – CCF/CTA Meeting, Barcelona, 26-28 October 2015
Ene_sim = Simulated energy
Ene_rec = Reconstructed energy
n = 1.00019 refractive index
ϑ = Cherenkov angle (ring radius)
For 50% of the events the error on the energy is lower than ~22%
where
E<20 GeV
For 50% of the events the error on the energy is lower than ~12% and for 80% of the events is lower that ~20%

## Slide 7
Results: Reconstruction error on the impact distance
T. Mineo – CCF/CTA Meeting, Barcelona, 26-28 October 2015
Cor_sim = Simulated impact distance
Cor_rec = Reconstructed impact distance
For 50% of the events the error on the impact distance is lower than ~20%

## Slide 8
Next Steps
T. Mineo – CCF/CTA Meeting, Barcelona, 26-28 October 2015
The aim of the following iteration is to reduce the reconstruction errors, compute the telescope efficiency and eventually increase the number of selected events (selection on x)
This analysis will includes:
an adequate cleaning of the image (see Cettina talk)
fit the ring using as seed the parameters (radius, center coordinate) derived in this first iteration
fit the distribution along the ring with a proper function that includes the shadow from the secondary mirror.