## Slide 1
CTA Calibration Meeting
Universidade de São Paulo
Instituto de Astronomia, Geofisica
e Ciencias Atmosferica
The ASTRI SST-2M Illuminator
Segreto, G. La Rosa
INAF Palermo
for the ASTRI Collaboration & the CTA Consortium

## Slide 2
the illuminator and the ASTRI-SST-2M calibration strategy
In support to the ASTRI SST-2M end-to-end calibration, a portable ground light source has been designed to illuminate the whole telescope aperture from several hundred meters distance
The ground light source will be used during the commissioning phase to measure the telescope actual spectral, temporal, spatial and linearity of the end-to-end response
Results will be used to:
  fine tuning the physical parameters of the ASTRI SST-2M Montecarlo code
  obtain, for each camera pixel, the end-to-end corrective factor for the flat fielding of sky images

## Slide 3
Illuminator position
2.1 km
The Illuminator will be positioned on the slopes of Mt. Etna, at km distance from the ASTRI SST 2M telescope location (Serra La Nave)

## Slide 4
The Illuminator
Light is generated inside the control box and delivered to the projection box through an optical fiber
A NIST calibrated photodiode inside the projection box is used to monitor the ouput light flux
A calibrated auxiliary telescope (UVscope) placed near the telescope aperture, allows to completely eliminate the uncertainty due to the atmospheric transmission
optical fiber
Time
Light generation and control box
auxiliary telescope (UVScope)
Projection-box
from NIST photodiode

## Slide 5
The Control Box
heavy duty, waterproof (IP67),
polypropylene case
43 cm
56 cm
86 cm
Ethernet
Control box interfaces

## Slide 6
Inside the control box
Local PC
RS232: 8
USB: 4
… plenty of room for:
battery pack
Wi-fi system
Optical generation devices
….
DC/AC inverter

## Slide 7
      Type: AGM (Absorbent Glass Mat)
      12V/100 AH
      323x170x214 mm
      32.8 Kg
The power box
Light generation and control box
Power box
AC Power Supply
DC Power Supply
The battery, currently installed inside the control box, makes it quite heavy and difficult to transport
  Battery will be moved on dedicated IP67 trolley-box
Projection box
CC 12 V
USB
fiber optic
CC

## Slide 8
The light projection box
The optical system is contained in a lightweight aluminium case that can be mounted on any common (manual or motorized) telescope mount for pointing
32 cm
18 cm
55 cm

## Slide 9
Illuminator status
The projection box of the Illuminator has been installed on a motorized mount ready to start laboratory tests on the projected beam
To be done before open-air nightly measurments:
  Water-tight box sealing
  Thermal insulation
  Heaters to prevent condensation
USB cable signals:
NIST sensor measurements
Photodiode Temperature
Humidity
Entrance window Temperature
Motorized Alt-Azimuthal mount
Fiber optic

## Slide 10
High Brightness LEDs
Relay array
Multicolor CW LED sources
LED current (rms <1‰) will be finely adjusted in order to keep the output light flux at the pre-selected level (<1‰)
Current control
LED selection
low noise (rms <1‰)
current generator
(2 A/15 V)
Light
(fiber optic)
Light intensity

## Slide 11
Multicolor LED sources
LED emitters are also available in the spectral region below 365 nm but it is TBV if their brightness (<25 mW/die) is enough for their use as light sources for the illuminator.
Visible: P >>1 W (<< 100 €)
365 nm
385 nm
395 nm
405 nm
UV-A (P > 1W) (100 €)
265 nm 10 mW: 1k€
280 nm 25 mW: 1k€
310 nm 25 mW: 1k€
340 nm 10 mW: 880 €
The visible and the UV-A (>365 nm) spectral region are rather well covered by High Brightness LEDs ( > 1W/die).

## Slide 12
The ns-pulsed source
ns-pulser
Variable pulse width:
from 2 ns in 1 ns step
USB 2.0 control
laser diode
Analog and digital modulation
Rise and fall time: < 2ns
Thermoelectric cooler (TEC)
Optical power: up to 200 mW
USB 2.0 and RS-232 control
Laser output
Input Trigger
2 ns
2 ns
Control of:
Pulse width
Repetition rate
Control of Laser current
Variable pulse length will allow to calibrate the camera timing response

## Slide 13
Requirements for additional light sources
The first Illuminator prototype will be equipped with:
- a single CW/ns pulsed laser light source (405 nm)
- a multi color HB LEDs CW/pulsed (obtainable pulse length TBV)
Other optical sources can be accommodated inside the illuminator control box provided they have:
  Compact and reasonable size
  Standard connector for fiber optic (e.g. SMA)
  Computer control via USB (or RS232)
  Precisely adjustable power
  Input for external trigger
  Standalone GUI (for Windows)
  Communication protocol manual (!)

## Slide 14
Possible ns-pulsed/multi-wavelength lasers system
Fiber optic Beam combiner
8 input – 1 output
Integrated 5 laser bay mount
Analog and digital control
USB and RS-232 interface for control from host computer
Example of available wavelengths:
375 nm 50 mW: 10k €
405 nm 100 mW: 5k €
445 nm 75 mW: 7k €
488 nm 50 mW: 6k €
640 nm 40 mW: 2k €

## Slide 15
ASTRI PSF vs. distance
PSF images and the relative radial distributions for an on-axis point sources placed at 400 m and 1.2 km from the ASTRI telescope aperture.
To limit the influence of the variable atmospheric attenuation, the illuminator could be placed at ≈ 1 km distance from ASTRI telescope aperture, obtaining a PSF good enough for an accurate verification of its Montecarlo model.
On-axis PSF at 1200 m
On-axis PSF at 400 m
(Logarithmic- scalee)
(Logarithmic- scalee)

## Slide 16
Calibration of the projected beam
A NIST calibrated photodiode inside the illuminator light-box continuosly monitor the light intensity at the entrance of its optical system
The projected light beam will be calibrated, as a function of wavelenght, by means of a 2nd NIST sensor (or a calibrated PMT), with a precision entrance pupil, placed at certain distance from the illuminator
To verify the spatial uniformity of the light beam, a 2D Azimuth/Elevation scanning will be performed by means of a motorized mount
Motorized Mount
«Reference» NIST sensor
photon flux:
light intensity
Precision Pinhole
R

## Slide 17
NIST-calibrated
Si Photodiode
Ø 9.5 mm
l: 200 nm – 1100 nm
50 nW – 50 mW
resolution: 1 nW
NTC Thermistor
Response Time: < 1 μs
Linearity: ± 0.5%
Measurement Uncertainty
  ±5% 200 – 450 nm
  ±3% 451 – 1000 nm
NIST reference
Spectral responce of the Si-photodiode used for the absolute calibration of the illuminator
Responsivity (A/W)
Quantum efficiency

## Slide 18
Summary
The ASTRI-SST 2M portable illuminating system
Projection box:
  Light weight, for easy installation on elevated (fixed or motorized) mounts
  output flux monitored by a NIST calibrated photodiode
  uniform far-field illumination pattern
Control box:
  battery powered
  computer with local control interfaces
  wireless system for remote control
  generation of ns-pulsed and CW light at several wavelengths
  adjustable pulse length (from 2ns in step of 1ns)
  continuously adjustable flux intensity