## Slide 1
CCF/CTA Calibration Meeting
T. Mineo– CCF/CTA Meeting, Barcelona, 26-28 October 2015
Pre-selection of muons: image statistics
Teresa Mineo, Cettina Maccarone
INAF/IASF-Palermo, Italy
for the ASTRI Collaboration & the CTA Consortium
Universidade de São Paulo
Instituto de Astronomia, Geofisica
e Ciencias Atmosferica

## Slide 2
Simulations
T. Mineo – CCF/CTA Meeting, Barcelona, 26-28 October 2015
CORSIKA |  | Proton | Muon
 | Site | Paranal | Paranal
 | spectral index | 2.7 | 2.0
 | energy range | 2-100 TeV | 6 GeV-1 TeV
 | Pointing | Zenith | Zenith
 | Viewcone | 4 deg | 4 deg
 | Max Distance | 400 m | 2.1 m
 | Starting altitude | free | 500 m above M1
 | N. Event | 100 000 | 200 000 (m+, m-)
 | Background | 20x106 ct/s/pixel | 20x106 ct/s/pixel
ASTRI-SIMULATOR: | includes the mirror reflectivity, the SiPM PDE, the PMMA window transmission, some of the mounting structure over the mirror |  | 
ANALYSIS SOFTWARE | IDL code |  | 

## Slide 3
Steps of the Analysis
T. Mineo – CCF/CTA Meeting, Barcelona, 26-28 October 2015
Proton
Muon
2) We computed the percentage of protons and muons contained in the interval where the muon distribution is higher than the proton one.
the maximum count in the pixels of each image
the number of pixel left after a given cut
the average of count left after the cuts.
We produced the histograms over all analysed events of the following variable:

## Slide 4
Cuts
T. Mineo – CCF/CTA Meeting, Barcelona, 26-28 October 2015
Proton
Muon
1)Cut with fixed number of count:
5, 7 and 10 counts
2)Cut with a number of count equal to 5xAverage, 7xAverage and 10xAverage.
This cut depends on the image statistics

## Slide 5
Results and Conclusion
T. Mineo – CCF/CTA Meeting, Barcelona, 26-28 October 2015
Cut | Proton | Muon
5 count | 32% | 91%
7 count | 42% | 92%
10 count | 37% | 92%
5xAverage | 37% | 92%
7xAverage | 39% | 93%
10xAverage | 31% | 84%
Selection on the average count after cut
Cut | Proton | Muon
5 count | 33% | 84%
7 count | 30% | 90%
10 count | 35% | 89%
5xAverage | 30% | 86%
7xAverage | 31% | 88%
10xAverage | 27% | 72%
Selection on the number of pixel after cut
Proton | Muon
36% | 92%
Selection on the maximum count
The investigated statistical parameters are not good for the pre-selection